## Slide 1: Trabajo final Arquitectura de computadoras Diseño del Sistema
Cesar Limones
Eduardo Michel

## Slide 2: System

## Slide 3: Peripheral component – Block Diagram
Peripheral
Send MSG command
From test bench
Read Data from file
PMC
Decoder
UART
Data
Addr
Bus req
Read
Write
Memory Controller
UART
MCP
Decoder
Data read
Error-retry
Ack
Wait-Bus busy

## Slide 4
Message codification
reg [15 : 0] iInstruction_tb;
reg [23 : 0] iAddr_tb;
reg [31 : 0] iData_tb;
Header :
  from peripheral
    read: 0x0001
    write 0x0002
  from mem controller
    wait: 0xFFF1
    ready 0xFFF2
    retransmit 0xFFF3
Start 1B | Header 2B | Data payload 7B = 4B Data 3B Addr| Error 1B| END 1B
oOutputMsg = {8'h0F, iInstruction, iData, iAddr, 7'b0, iError, 8'hF0};

## Slide 5
Peripheral component – Synthesis
UART control
Message is concatenated for UART
oOutputMsg = {8'h0F, iInstruction, iData, iAddr, 7'b0, iError, 8'hF0};
Flags from decoder and UART
Output to TB
Output to TB
Output to UART
Instructions/data/addr from TB
Data decoded from MCP decoder

## Slide 6
Peripheral component FSM – Synthesis
CONFIRM: waits for Message (decoded by MCP decoder)
RETRY: If MC replies with WAIT or ERROR-Retransmit, retry goes to MSG again, latched messga is sent again
RECEIVE: If MC replies with ACK latches DATA & ready if READ instruction or Ready if WRITE instruction.
LOAD: Latches Data, ADDR, Instr and Error from TB
MSG: Sends msg to UART, waits for UART ACK TxDone

## Slide 7
Decoder PMC
UART control
Message is concatenated for UART
oOutputMsg = {8'h0F, iInstruction, iData, iAddr, 7'b0, iError, 8'hF0};
Flags from decoder and UART
Output to TB
Output to TB
Output to UART
Instructions/data/addr from TB
Data decoded from MCP decoder

## Slide 8: Peripheral component – Verification cases
Peripheral memory read – No error, cache miss/ cache hit clean
Peripheral memory write – No error, cache miss/ cache hit clean
Peripheral memory read – No error, cache hit Modified with retry
Peripheral memory write – No error, cache hit Modified with retry
Peripheral memory read – Error
Peripheral memory write – Error
Peripheral tries to read/write but bus held by MC.
Peripheral tries to read/write but bus held by CPU, thru MC.

## Slide 9: Peripheral memory write – No error, cache miss/ cache hit clean

## Slide 10: Peripheral memory Read–error: retry message from MC, successful retry

## Slide 11: Memory controller
Memory Controller
Serial communication with peripheral
Address/data Bus to Main Memory
To CPU:
Address/data Bus
Control Signals Bus

## Slide 12: Memory controller – Control signals
AHOLD – address hold: maintain memoryconsistency
• EADS# - external address strobe: external; informs the processor of a valid address on its local bus to be snooped (internal cache lookup)
• input INV – invalidate: external; informs the processor to leave cache line valid or mark it invalid on a snoop hit
• inout HIT# - hit on internal cache – notify other processors that information is shared by another cache
• inout HITM# - hit modified line: hit to a modified line incache, write-back required
PBGNT# - private bus grant: asserted to grant bus ownership
• inout PBREQ# - private bus request: asserted to request bus ownership

## Slide 13: Memory controller– Verification cases CPU
Cache Snoop – miss
Cache Snoop – Hit Clean
Cache Snoop – Hit Modified.
  Write back.
Test all control signals.

## Slide 14: Memory controller– Verification cases Peripheral
Reject peripheral request, bus held by CPU or MC.
Handle Peripheral memory write – No error, cache miss/ cache clean hit
Handle Peripheral memory read– No error, cache miss/ cache clean hit
Handle Peripheral memory read – No error, cache hit Modified with retry
Handle Peripheral memory write – No error, cache hit Modified with retry
Handle Peripheral memory read – Error
Handle Peripheral memory write – Error

## Slide 15: Main Memory
Main Memory
Address/data Bus to Memory controller
Write Enable
Implement single port RAM with WE and MESI bits

## Slide 16: Main Memory Verification Cases
Read
Write
Modify MESI bits.

## Slide 17: CPU
CPU
To Memory controller:
Address/data Bus
Control Signals Bus

## Slide 18: CPU
CPU reads file from computer that contains instructions to:
read/write - header
addresses
Data
Error bits generated arbitrarily
CPU state machine parses data from file simulating processing outputs and coordinates with Memory controller using control Bus signals to read/write from main memory.

## Slide 19: CPU Verification cases
Parse files
Read from Cache
Read from main memory
Write to cache
Write to main memory

## Slide 20: Cache
Cache
To Memory controller:
Address/data Bus
Control Signals Bus
Cache design is practically given in the final project description.

## Slide 21: Cache Verification cases
Read from Cache
Write to cache
Snoop
  Miss
  Hit Clean
  Hit Modified

## Slide 22: Backup

## Slide 23: Peripheral component
UART
To memory controller
Peripheral reads file from computer that contains instructions to:
read/write - header
addresses
Data
Error bits generated arbitrarily
Peripheral state machine parses data and forms message as per format below.
Waits for send command.
Send command moves message to UART and sends to Mem Controller.
MSG
Buffer

## Slide 24: Memory controller
UART
MC state machine parses message from Peripheral.
If conflict with address bus request, gives access to CPU and notifies Peripheral to resend msg after waiting.
If Bus is free sends address to Cache to start snoop operation and reads control signals.
Serial from peripheral